## Slide 1
"Forecasting Electricity Generation and Consumption in Bangladesh: A Comparative Study of ARIMA, VECM, and LSTM Models"
Presented By
Md Forhad Hosen
ASH2015026M
Presentation on

## Slide 2
Introduction
Accurate electricity forecasting is essential for Bangladesh's energy planning, given rapid population growth, urbanization, and industrialization. Electrification has reached 99.5% in 2023, and installed capacity has expanded significantly. However, overestimating or underestimating demand can lead to supply shortages or excessive investments, impacting the economy. This study compares three forecasting models — ARIMA, VAR, and LSTM — to predict electricity generation and consumption, aiming to support policy decisions and infrastructure planning.
Over Consumption Problems
Supply Shortages
Increased Costs
Resource Depletion
Environmental Impact
Grid Instability
Economic Strain
Over Generation Problems:
Overcapacity
Financial Burden
Environmental Impact
Higher Operational Costs
Resource Wastage
Page 01

## Slide 3
Research Objectives
Page 02
01
To explore historical trends in electricity generation and consumption.
02
To develop and validate time-series forecasting models.
To compare the performance and accuracy of ARIMA, VECM, and LSTM models.
03
To generate short-term forecasts for the period 2024–2028.
04

## Slide 4
Research Gap
Page 03
  Few studies have compared ARIMA, VAR, and LSTM models using a unified dataset for Bangladesh.
  Hybrid models combining these methods remain underexplored. This study addresses these gaps by evaluating all three models on Bangladesh’s historical data (1971–2023).

## Slide 5
Page 04
01
Data Collection
Bangladesh Power Development Board (BPDB) and Bangladesh Bureau of Statistics (BBS). It includes historical electricity generation and consumption data, along with socio-economic factors like GDP, population, and per capita consumption, covering the period from 1971 to 2023.
02
Software and Tools
Data analysis and modeling were conducted using Python (version 3.11.13).
03
ARIMA , VAR , LSTM are use for modeling and forecasting electricity Generation and consumption.
ARIMA: A statistical method suitable for linear time series data.
VECM: A model that captures long-term relationships among multiple variables like GDP and electricity generation.
LSTM: A deep learning model for capturing complex, nonlinear patterns in time series data.
Methodology
Methods

## Slide 6
Page 05
Data Analysis And Results
  Electricity Consumption (ARIMA)
  select P, q from ACF and PACF
  Best model: ARIMA(2,2,0)
  AIC: 822.745930
  BIC: 828.541407
  RMSE: 719.77
  MAE: 502.35
  Ljung-Box Test p-value: 0.8231

## Slide 7
Page 06
Data Analysis And Results
  Electricity Consumption (VAR)
VAR model include variable net consumption ,net generation and GDP . All variable data are non stationary . After 1st differencing data does not become stationary .
Optimal lag order of 3 based on AIC and BIC.
Then perform Johansen Cointegration Test and its confirm that data are cointegrated.
RMSE 450.08, MAE 263.88

## Slide 8
Page 07
Data Analysis And Results
  Electricity Consumption (LSTM)
The combination of time steps = 4 and 100 epochs in this LSTM model has Low RMSE and MAE
The combination of time steps and epochs

## Slide 9
Page 08
Data Analysis And Results
  Forecasting Electricity Consumption using Best Model
Model comparison for Net consumption data
VECM is a great choice for forecasting net electricity consumption.
steady increase in net consumption over time.

## Slide 10
Page 09
Data Analysis And Results
  Electricity Generation (ARIMA)
  select P, q from ACF and PACF
  Best model: ARIMA(2,2,2)
  AIC: 852.40432
  BIC: 862.063454
  RMSE: 912.26
  MAE: 596.19
  Ljung-Box Test p-value: 0.7731

## Slide 11
Page 10
Data Analysis And Results
  Electricity Generation (VAR)
VAR model include variable net consumption ,net generation and GDP . All variable data are non stationary . After 1st differencing data does not become stationary .
Optimal lag order of 3 based on AIC and BIC.
Then perform Johansen Cointegration Test and its confirm that data are cointegrated.
RMSE 1193.72, MAE 598.63

## Slide 12
Page 11
Data Analysis And Results
  Electricity Generation (LSTM)
The combination of time steps = 5 and 100 epochs in this LSTM model has Low RMSE and MAE
The combination of time steps and epochs

## Slide 13
Page 12
Data Analysis And Results
  Forecasting Electricity Generation using Best Model
Model comparison for Net consumption data
ARIMA is a great choice for forecasting net electricity consumption.
steady increase in net consumption over time.

## Slide 14
Page 13
Data Analysis And Results
  Forecasted yearly Electricity Generation And consumption Value

## Slide 15
Page 14
  ARIMA provides the most accurate results for predicting electricity generation in Bangladesh due to its simplicity and efficiency.
  VAR/VECM captures complex factors affecting electricity consumption, offering a detailed understanding.
  Forecasts indicate a rise in electricity generation and consumption, requiring increased infrastructure investment to meet growing demand.
  Future studies could focus on improving LSTM models, incorporating renewable energy sources, and assessing environmental impacts for a more comprehensive outlook on Bangladesh's energy future
Conclusion

## Slide 16
Page 15
Limitations of the Study
  Annual Data Only : Using yearly data (1971–2023) masks seasonal, monthly, daily demand fluctuations critical for operational planning.
  Small Sample for Deep Learning: With only 53 observations, LSTM models risk overfitting and may not capture genuine patterns.

## Slide 17
Thank You